## Slide 1: Revisiting Statically Determinate systems on the way to Statically Determinate systems
We will begin with problems in one dimension.
That is where we have dealt with one unknown reaction (constraint) only.

## Slide 2: What is a statically determinate system ?
A simple answer, within the context of what we learn in first year mechanics, is when the number of unknown reactions (constraints) is equal to the number of equations of static equilibrium that we can obtain from the system. Hence number of (generalized) FORCE equilibrium equations must be equal to number of unknown reactions. Why GENERALIZED ? Because this definition will then also consider Moments of a force and Moment reactions.

## Slide 3: Relation with dimensions
A one dimensional problem will have only one equilibrium equation. Rotation requires at least two dimensions. In a one dimensional system only possible motion is translation along one given direction. Hence the only possible reaction required to make the system static is also a force in that direction (actually in the opposite or negative with respect to that direction).

## Slide 4: A one dimensionsal problem
We have a rod with one end fixed to a wall and a force P pulling it at the free end. We can figure out the reaction at the wall simply by looking at the problem but we will take a more formal, long winded approach, which will become inevitable as the problems become more complicated.
P

## Slide 5: A one dimensionsal problem
We start with the free body diagram and replace the constraint (the fixed joint at the wall) with its effect, namely the reaction force R.
P
R

## Slide 6: A one dimensionsal problem
We now apply the equation of equilibrium and get P+R=0, which tells us that R=-P. The problem is solved and it should be because it is statically determinate.
P
R

## Slide 7: A one dimensionsal problem
We now consider a case where the bar is fixed at both the ends. The force P acts at the same point. The drawing has been changed slightly only to ensure the clarity of the picture.
P

## Slide 8: A one dimensionsal problem
We draw the free body diagram as before. Since there are fixed joints at both ends we will get one more reaction force Q
P
R
Q

## Slide 9: A one dimensionsal problem
We apply the equation of equilibrium and get P+Q+R=0, which tells us that R+Q=-P. So we know the sum of the two unknown reactions but we do not know the value of either P or Q. We cannot proceed further because we have no more equilibrium equations in the bank. Hence this problem is statically indeterminate
P
R
Q

## Slide 10: A one dimensionsal problem
We need something more. To get this something more we will solve a few complicated versions of the original problem.
P
R
Q

## Slide 11: Change in length
The something more will come from the change in geometry due to deformation. In one dimension, there is only one relevant geometrical feature, which is the length of the bar L.
P
R
L

## Slide 12: Change in length
We will focus on finding the deformation DL
P
R
L
DL

## Slide 13: Find the internal force
We first label the two ends of the rod as A and B and set up a coordinate system. A is the origin with the direction from A to B being positive.
P
R
DL
x
A
B

## Slide 14: Take a section
We take a section at a distance x from the origin.
P
R
DL
x
A
B

## Slide 15: Take a section
We take a section at a distance x from the origin. That is we cut the rod at a distance x. What we will be seeing is a force perpendicular to the exposed surface, which may or may not be dependent on x. We will call it F(x) to indicate that it is a function of x (remember that a constant value can also be considered a special case of a function of x).
F(x)
R
x
A

## Slide 16: Take a section
Simple equilibrium of forces tells us that F(x)=-R. Since we already know that R=-P, hence F(x)=P. We also draw a graph of our results.
F(x)
R
A
x
F(x)
L
P
x

## Slide 17: Revisiting stress
It is now easy to find the stress at any x as long as we know the area of cross section at that x, which is A(x). Once again A(x) may or may not be a constant. And we quickly draw a graph of s(x) for our particular problem where A is a constant and hence s(x) =P/A.
s(x)= F(x)/A(x)
x
s(x)
L
s

## Slide 18: Revisiting Hooke’s law
We can now use Hooke’s law to find strain at any x provided we know the modulus of elasticity E at that x, which is E(x). Once again E(x) may or may not be a constant (the rod can be made of two different materials). And we quickly draw a graph of e(x) for our particular problem where E is a constant and hence e(x) =P/[EA].
e(x)= s(x)/E(x)
=F(x)/[E(x)A(x)]
x
e(x)
L
e

## Slide 19: Revisiting definition of strain
We may recall that u(x) is a function defining the displacement of a point at x on the rod due to the application of the external force P. Strain is defined in terms of that displacement or to be more precise the gradient or rate of change of that displacement with respect to x.
e(x)= du(x)/dx
x
e(x)
L
e

## Slide 20: Explanation of u
Consider two points on the rod C and D whose coordinates are xC and xD. After being pulled by the force P, C will be displaced by an amount uC and D will be displaced by an amount uD. This amount MAY NOT be the same for C and D. It depends on what are the external forces , where they are applied as well as the material and dimensions of the rod. This will become clear when we consider a rod with different materials and/or different cross sections at different x.
C
D
C
D

## Slide 21: Explanation of u
A rough estimate of strain is then = (uD-uC)/(xD-xC)
When C and D are very close together it becomes du/dx
C
D
C
D

## Slide 22: Equating the two expressions for strain
e(x) =du(x)/dx=F(x)/[E(x)A(x)]
For our simple case
e(x)= du(x)/dx=F/[EA]

## Slide 23: Equating the two expressions for strain
For our simple case F, E, A are constants

## Slide 24: Total elongation
For our simple case the total elongation or change of length of the rod will be simply the displacement of the point B
This is a very familiar high school formula. But the relatively complicated derivation will pay off when the problems are complicated.

## Slide 25: How does this help with indeterminate problems ?
To answer this question we will add a simple twist to our initial simple question. What is the force Q required at the free end so that P produces zero elongation at that end ?
P
Q

## Slide 26: Back to the original problem
What does the second wall do ? It produces a reaction Q that ensures that there is no displacement at the second wall. Now ask the question. Is the problem in the previous slide the same but with some phrases being different ?
P

## Slide 27: A more realistic problem
The force P is now acting at the midpoint of the rod, which is fixed at both ends. The task ahead is to find out the reactions at A and B.
P
A
C
B

## Slide 28: Start with FBD
First set up a coordinate system. In this case the origin can be at A and the +ve direction will be from A to B
The reactions will be RA and RB. The directions shown have intentionally been kept positive, although they are counterintuitive. You would certainly have liked at least one of them to have a direction opposite to P. But as we work with complicated problems we will find this has advantages. Once we get the answers the signs will tell us the directions.
P
RA
C
RB
x

## Slide 29: The alternative problem
We will try to solve the following problem. What should be RB so that the displacement at point B is zero ?
P
C
RB
x
B
A

## Slide 30: FBD of the alternative problem
The free body diagram comes out to be the same
P
RA
C
RB
x

## Slide 31: Critical Points and Domains
A critical point is a point where there is a sudden change - in forces, in dimensions, in material properties, or there is new constraint. Here we have three critical points A, C and B and hence two domains – A to C and C to B.
We will need to take a section in every domain
P
RA
C
RB
x

## Slide 32: Domain AC: Force
P
C
RB
Once we cut the section we will see an internal force F(x) at the cut. Using equilibrium (ONLY FOR THE SECTION UPTO x) we will get
RA
x
F(x)

## Slide 33: Domain AC: Stress
P
C
RB
Area of cross section is A for the entire rod. So
RA
x
F(x)

## Slide 34: Domain AC: Strain
P
C
RB
Modulus of elasticity is E for the entire rod. So
RA
x
F(x)

## Slide 35: Domain AC: Displacement
P
C
RB
Hence
RA
x
F(x)

## Slide 36: Domain CB: Force
C
RB
Once we cut the section between C and B we will see an internal force F(x) at the cut.
Note that in this domain we can now see P, but RB still remains hidden. Also origin and coordinate system remain unchanged.
Using equilibrium we get
RA
x
F(x)
P

## Slide 37: Domain CB: Stress
Area of cross section is A for the entire rod. So
C
RB
RA
x
F(x)
P

## Slide 38: Domain CB: Strain
Modulus of elasticity is E for the entire rod. So
C
RB
RA
x
F(x)
P

## Slide 39: Domain CB: Displacement
Here we need to understand that the domain of integration must span both AC and CB since integration is from 0 to x and now x spans both domains. We will need to split the interval of integration into two intervals and use the expressions for e(x) derived for the domains AC and CB.
C
RB
RA
x
F(x)
P

## Slide 40: Domain CB: Displacement
We can now calculate the displacement at x in domain CB. Since C is the midpoint xc = L/2
C
RB
RA
x
F(x)
P

## Slide 41: Displacement at B
We can now calculate the displacement at B, xB = L
C
RB
RA
x
F(x)
P

## Slide 42: Displacement at B
But we wish that uB = 0
C
RB
RA
x
F(x)
P

## Slide 43: Equilibrium for the whole bar
Force equilibrium gives us
But we already know
C
RB
RA
x
P

## Slide 44: A more complicated problem
The force P is acting at the free end C of the rod, which is fixed to a wall at end A. At the midpoint B the rod passes through a hole in another wall, ensuring that point B does not move. Length of AB=length of BC=L/2. Area of cross section for AB = 2a. Area of cross section for BC = a. Modulus of elasticity for both segments is E. We are required to find the reactions.
P
A
B
C

## Slide 45: Start with FBD
First set up a coordinate system. In this case the origin can be at A and the +ve direction will be from A to B
The reactions will be RA and RB. The directions shown have intentionally been kept positive, although they are counterintuitive. You would certainly have liked at least one of them to have a direction opposite to P. But as we work with complicated problems we will find this has advantages. Once we get the answers the signs will tell us the directions.
RA
x
P
A
B
C
RB

## Slide 46: The alternative problem
We will try to solve the following problem. What should be RB so that the displacement at point B is zero ?
x
P
A
B
C
RB

## Slide 47: FBD of the alternative problem
The free body diagram comes out to be the same
RA
x
P
A
B
C
RB

## Slide 48: Critical Points and Domains
A critical point is a point where there is a sudden change - in forces, in dimensions, in material properties, or there is new constraint. Here we have three critical points A, B and C and hence two domains – A to B and B to C.
We will need to take a section in every domain
RA
x
P
A
B
C
RB

## Slide 49: Domain AB: Force
Once we cut the section we will see an internal force F(x) at the cut. Using equilibrium (ONLY FOR THE SECTION UPTO x) we will get
x
RA
P
A
B
C
RB
F(x)

## Slide 50: Domain AB: Stress
Area of cross section is 2a from A to B. So
RA
P
A
B
C
RB
F(x)
x

## Slide 51: Domain AB: Strain
Modulus of elasticity is E for the entire rod. So
RA
P
A
B
C
RB
F(x)
x

## Slide 52: Domain AB: Displacement
Hence
RA
P
A
B
C
RB
F(x)
x

## Slide 53: Domain BC: Force
Once we cut the section between B and C we will see an internal force F(x) at the cut.
Note that in this domain we can now see RB, but P still remains hidden. Also origin and coordinate system remain unchanged.
Using equilibrium we get
RA
P
A
B
C
RB
F(x)
x

## Slide 54: Domain BC: Stress
Area of cross section is a from B to C. So
RA
P
A
B
C
RB
F(x)
x

## Slide 55: Domain BC: Strain
Modulus of elasticity is E for the entire rod. So
RA
P
A
B
C
RB
F(x)
x

## Slide 56: Domain BC: Displacement
Here we need to understand that the domain of integration must span both AC and CB since integration is from 0 to x and now x spans both domains. We will need to split the interval of integration into two intervals and use the expressions for e(x) derived for the domains AB and BC.
RA
P
A
B
C
RB
F(x)
x

## Slide 57: Domain BC: Displacement
We can now calculate the displacement at x in domain BC. Since B is the midpoint xB = L/2
RA
P
A
B
C
RB
F(x)
x

## Slide 58: Displacement at B
We can now calculate the displacement at B, xB = L/2 by using any of the two expressions for u(x). First we use the expression for domain AB
RA
P
A
B
C
RB
x

## Slide 59: Displacement at B
Next we use the expression for domain BC
As it MUST be, both answers are same
RA
P
A
B
C
RB
x

## Slide 60: Displacement at B
But we wish that uB = 0
RA
P
A
B
C
RB
x

## Slide 61: Equilibrium for the whole bar
Force equilibrium gives us
But we already know
RA
P
A
B
C
RB
x

## Slide 62: Displacement at C
We have to use the expression for domain BC and use xc=L
RA
P
A
B
C
RB
x

## Slide 63: Displacement at C
We can also solve the problem by recognizing that at C also there is no movement. Hence
RA
P
A
B
C
RB
x

## Slide 64: Another complicated problem
The force P is acting at the free end A of the rod, which is fixed to a wall at end C. At the midpoint B the rod passes through a hole in another wall, ensuring that point B does not move. A force Q acts at B. Length of AB=length of BC=L/2. Area of cross section for AB = 2a. Area of cross section for BC = a. Modulus of elasticity for AB = E. Modulus of elasticity for AB = 2E. We are required to find the reactions.
A
C
P
Q
B

## Slide 65: Start with FBD
First set up a coordinate system. In this case the origin can be at B (not A, since A will be moving) and the +ve direction will be from B to C
The reactions will be RB and RC. The directions shown have intentionally been kept positive, although they are counterintuitive. You would certainly have liked at least one of them to have a direction opposite to P. But as we work with complicated problems we will find this has advantages. Once we get the answers the signs will tell us the directions.
RC
A
C
Q
B
RB
P
x

## Slide 66: The alternative problem
We will try to solve the following problem. What should be RC so that the displacement at point C is zero ?
A
C
Q
B
RB
P
x

## Slide 67: FBD of the alternative problem
The free body diagram comes out to be the same
RC
A
C
Q
B
RB
P
x

## Slide 68: Critical Points and Domains
A critical point is a point where there is a sudden change - in forces, in dimensions, in material properties, or there is new constraint. Here we have three critical points A, B and C and hence two domains – A to B and B to C.
We will need to take a section in every domain
RC
A
C
Q
B
RB
P
x

## Slide 69: Domain AB: Force
Once we cut the section we will see an internal force F(x) at the cut. Using equilibrium (ONLY FOR THE SECTION UPTO x) we will get
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 70: Domain AB: Stress
Area of cross section is 2a from A to B. So
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 71: Domain AB: Strain
Modulus of elasticity is E for AB. So
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 72: Domain AB: Displacement
Here xA=-L/2. Not that we are moving from the origin upto our x only, (which is on the negative side of the origin but the sign is automatically taken care of), and not necessarily upto A. Hence
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 73: Domain BC: Force
Once we cut the section between B and C we will see an internal force F(x) at the cut.
Note that in this domain we can now see Q and RB, but RC still remains hidden. Also origin and coordinate system remain unchanged.
Using equilibrium we get
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 74: Domain BC: Stress
Area of cross section is a from B to C. So
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 75: Domain BC: Strain
Modulus of elasticity is 2E from B to C. So
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 76: Domain BC: Displacement
Here we need to understand that the domain of integration does not need to span AB since integration is from 0 to x and now x spans only BC. We will not need to split the interval of integration into two intervals.
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 77: Domain BC: Displacement
We can now calculate the displacement at x in domain BC. Since xB = 0
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 78: Displacement at B
We can now calculate the displacement at B, where x = 0, by using any of the two expressions for u(x).
Either way we get
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 79: Displacement at B
We can now calculate the displacement at B, where x = 0, by using any of the two expressions for u(x).
Either way we get
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 80: Displacement at B
Equating these two zeros would lead to the wrong conclusion shown below.
We should only conclude that since the constraint is getting satisfied we are not getting useful information from x=0
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 81: Displacement at C
We therefore look at C, where x = L/2. We get
Q
RC
A
C
B
RB
P
F(x)
x

## Slide 82: Equilibrium for the whole bar
Force equilibrium gives us
But we already
Hence
Q
RC
A
C
B
RB
P
x