## Slide 1: Shear Stresses in Transversely Loaded Beams

## Slide 2: Shear Stresses in Beams
We will consider a beam with a distributed load in the neighbourhood of point C as shown
The transverse section of the beam at C and the coordinate system is shown in the picture on the right.
z
y
C
w (x)

## Slide 3: Shear Stresses in Beams
Now we will consider another point D, very close to C.
Since the point is close to C, the nature of load, material properties and cross section will change very little.
z
y
C
w (x)
D

## Slide 4: Shear Stresses in Beams
Next we take a magnified view of the beam around CD. Our x axis is positive from C to D.
The distance between C and D is Dx.
The neutral axis is at c from top
z
y
c
x
C
D
Dx
Neutral Axis

## Slide 5: Shear Stresses in Beams
We now consider two points C’ and D’ right below C and D and at a distance y1 from the neutral axis.
We will take this chunk out of the beam and see what forces act on it.
z
y
y1
c
C’
D’
x
C
D
Dx
Neutral Axis

## Slide 6: Shear Stresses in Beams
Here is how things look like when the chunk is still attached to the beam
We see a load wDx acting vertically downward on the exposed surface CD
C
D
wDx
C’
D’

## Slide 7: Shear Stresses in Beams
We now remove the part of the beam attached to the bottom C’D’
We will now see the shear force DH which was holding the bottom of the chunk to the rest of the beam and preventing it from sliding in the process of bending.
The obvious question is what about vertical forces ?
We will answer that next.
C
D
wDx
C’
D’
DH
H=Horizontal shear force

## Slide 8: Shear Stresses in Beams
We now detach the side walls i.e. CC’ and DD’ from the beam.
Now the chunk is completely free of the beam
We get to see the vertical shear forces acting on the side walls.
These are the forces that were preventing the chunk from popping out of the beam while bending.
C
D
wDx
C’
D’
DH
VC
VD
Vertical normal stresses are much smaller. So we are ignoring them. We have already encountered these vertical forces when drawing SFD for beams.

## Slide 9: Shear Stresses in Beams
We also get to see the internal normal stresses that arise due to bending.
These are the stresses we have already encountered while studying bending of beams.
Since the external forces are downwards hence the beam will be compressed at the top. Hence the stresses are compressive.
C
D
wDx
C’
D’
DH
VC
VD

## Slide 11: Shear Stresses in Beams
The normal stresses on the walls CC’ and DD’ at any point a distance y from the neutral axis are given by
C
D
wDx
C’
D’
DH
VC
VD
Neutral Axis
y1
y

## Slide 12: Shear Stresses in Beams
Hence the total force due to these stresses on the side walls up to a distance y is
C
D
wDx
C’
D’
DH
VC
VD
Neutral Axis
y1
y

## Slide 13: Shear Stresses in Beams
Let us now do the force balance in the y direction.
Since Dx is small we can ignore change in area of cross section between C and D.
We get
C
D
wDx
C’
D’
DH
VC
VD

## Slide 14: Shear Stresses in Beams
We can now substitute for the stresses using the formula
If Dx is small then
C
D
wDx
C’
D’
DH
VC
VD

## Slide 15: Shear Stresses in Beams
We need to note some important points regarding how what we have done so far differs from what we usually do in our normal stress problem solving ?
First, we are not integrating over the entire cross section of the beam but from C’ to C.
But the I that we are using is for the entire cross section.
It is not the second moment of the area between C and C’ or D and D’.
This is because the formula for stress at any y uses the I for the entire cross section only. The I does not depend on y but on x.
If Dx is small then
C
D
wDx
C’
D’
DH
VC
VD

## Slide 16: Shear Stresses in Beams
Let us now recall a few points about moments and shear forces in beams.
We consider a section of the beam in the neighbourhood of C extending across the full depth of the beam.
The directions of the moments have been set such that the top part of the beam is in compression
The internal forces and moments change by DV and DM respectively as we shift by Dx.
C
D
wDx
Dx
V
M
V+DV
M+DM

## Slide 17: Shear Stresses in Beams
First we consider the equilibrium in y direction
C
D
wDx
Dx
V
M
V+DV
M+DM

## Slide 18: Shear Stresses in Beams
Next we consider moment equilibrium about C

## Slide 19: Shear Stresses in Beams
In case of the present problem we have already obtained
If Dx is small then in the limit
C
D
wDx
C’
D’
DH
VC
VD

## Slide 20: Shear Stresses in Beams
We also know from our previous experience with SFD and BMD and our revision of bending in beams that
Hence
C
D
wDx
C’
D’
DH
VC
VD

## Slide 21: Shear Stresses in Beams
Let us try to understand this new quantity
Let us look at our initial diagrams of the beam. Q is the first moment of the dark shaded area in the second figure. Hence if that area is Aa and the centroid of that area has a y coordinate ya then
z
y
y1
c
C’
D’
x
C
D
Dx
Neutral Axis
ya

## Slide 23: Shear Stresses in Beams
We can now define a quantity called shear flow by considering the width of the shaded area.
t
DH
Dx
a
t
z
y
y1
c
C’
D’
x
C
D
Dx
Neutral Axis
t

## Slide 24: Shear Stresses in Beams
The shear stress is simply DH divided by the area on which it is acting i.e. tDx.
This should also answer the question why we call these vertical forces in beams as shear forces. They cause shear stress.
t
DH
Dx
a
t
z
y
y1
c
C’
D’
x
C
D
Dx
Neutral Axis
t