## Slide 1: Statically indeterminate problems
Axial loading - I

## Slide 2: Statically indeterminate problems we have already done without even knowing that they were so
Consider a solid cylinder of material 1 within a hollow cylinder of material 2. They are bonded together so that they cannot slip at the contacting surface.

## Slide 3: Statically indeterminate problems we have already done without even knowing that they were so
Now fix the bottom surface of both cylinders, and fix a rigid plate to the top surface. At both ends the two cylinders are bonded rigidly to those two surfaces. Thus if the plate moves up, the bonded surfaces of both cylinders move by the same amount.

## Slide 4: Statically indeterminate problems we have already done without even knowing that they were so
The plate is now pulled by a force P at point A which is the center of the plate. Point B is the center of the bottom part of the cylinders.
P
A
B

## Slide 5: Statically indeterminate problems we have already done without even knowing that they were so
Free Body Diagram of the entire contraption
P+R=0
R=-P
P
A
B
R

## Slide 6: Statically indeterminate problems we have already done without even knowing that they were so
Free Body Diagram of plate
P
A
B
R

## Slide 7: Statically indeterminate problems we have already done without even knowing that they were so
Free Body Diagram of plate and the two cylinders taken together as one. We have used the fact that R=-P.
P
A
B
P
P
P

## Slide 8: Statically indeterminate problems we have already done without even knowing that they were so
Free Body Diagram of each cylinder? (Why the question mark ?)
Because it is here that we face the problem of indeterminacy
All we know is P1+ P2 = P
P2
P2
P1
P1

## Slide 9: Statically indeterminate problems we have already done without even knowing that they were so
What is the geometrical constraint ?
Since the top plate is rigid and is rigidly attached to both cylinders and both cylinders are rigidly bonded to each other, the displacement of the top surface for both cylinders must be same under the action of P.
P2
P2
P1
P1

## Slide 10: Statically indeterminate problems we have already done without even knowing that they were so
Let the areas of cross section of the cylinders be a1 and a2 and the moduli of elasticity be E1 and E2. Let the length of the combined cylinder be L.
P2
P2
P1
P1

## Slide 11: Statically indeterminate problems we have already done without even knowing that they were so
For outer cylinder, the displacement of point A with respect to B will be
uAB1 = P1L/(E1a1)
P1
P1

## Slide 12: Statically indeterminate problems we have already done without even knowing that they were so
For inner cylinder, the displacement of point A with respect to B will be
uAB1 = P2L/(E2a2)
P2
P2

## Slide 13: Statically indeterminate problems we have already done without even knowing that they were so
Applying geometrical constraint uAB1 = uAB1
We have P1L/(E1a1)=P2L/(E2a2)
Hence
P1=P2(E1a1)/(E2a2)
P2
P2
P1
P1

## Slide 14: Statically indeterminate problems we have already done without even knowing that they were so
But P1+ P2=P
Hence
P2(E1a1)/(E2a2) + P2 = P
So
P2 = PE2a2/(E1a1+E2a2)
P1 = PE1a1/(E1a1+E2a2)
P2
P2
P1
P1

## Slide 15: Statically indeterminate problems we have already done without even knowing that they were so
Have we done this before ?
Yes! When we solved for springs in parallel in high school we were actually solving a statically indeterminate problem. Nobody uses that term in high school, that is all.
This contraption is actually two springs in parallel, with one spring being inside another.

## Slide 16: Rigid Rod hanging from wires
We first start with a version of the problem that is statically determinate.
A rigid rod with center of mass at G of weight W is hanging from 2 flexible wires of unstretched length L and area of cross section a each attached at A and B and made of material with modulus of elasticity E. Length of the rigid rod is S. We need to find the tension in each wire when the contraption is in static equilibrium. AB=S/3
A
B
G

## Slide 17: Rigid Rod hanging from wires
We get from the FBD of wires and the rod the following force equilibrium equation
TA+TB = W
Taking moments about A, we get
TBS/3 = WS/2
We have two unknowns TA and TB
We have two equations
Thus the problem is determinate.
A
B
G
TA
TB
TA
TB
TA
TB
W

## Slide 18: Rigid Rod hanging from wires
We now make this problem a version of the problem statically indeterminate by adding another wire identical to the other two at C. We set BC=S/3
A
B
G
C

## Slide 19: Rigid Rod hanging from wires
We get from the FBD of wires and the rod the following force equilibrium equation
TA+TB+TC = W
Taking moments about A, we get
TBS/3+ 2TCS/3 = WS/2
We have three unknowns TA,TB,TC.
We still have two equations only
Thus the problem is cannot be solved as is and is indeterminate.
A
B
G
TA
TB
TA
TB
TA
TB
TC
TC
TC
W

## Slide 20: Rigid Rod hanging from wires
We now look at the deformed shape of the contraption. Note that we have assumed that the wires are still vertical and all the points are moving down almost vertically. This is a reasonable assumption if the movement is small. The deformations shown in the figure are of course highly exaggerated.
A’
B’
C’
G’
A
B
G
C
q

## Slide 21: Rigid Rod hanging from wires
From our knowledge of elastic deformation we know
A’
B’
C’
G’
A
B
G
C
q

## Slide 22: Rigid Rod hanging from wires
From geometry we have
A’
B’
C’
G’
A
B
G
C
q

## Slide 23: Rigid Rod hanging from wires
Combining this knowledge we get
A’
B’
C’
G’
A
B
G
C
q
We thus have our third equation

## Slide 24: Rigid Rod hanging from wires
Force equilibrium equation
TA + TB + TC = W
Moment equilibrium equation
TBS/3 + 2TCS/3 = WS/2
From geometrical constraint and deformation
TA + Tc = 2TB
Hence
TB = 4W/12, TC = 7W/12, TA =W/12
.

## Slide 25: An added twist
The wire at C is replaced by a rope which is initially slack and because it is longer than the wires by an amount d. At equilibrium the rope is tight. Material properties of the rope and area of cross section are the same as that of the wires.
A
B
G
C

## Slide 26: An added twist
In this case CC’ will have two parts.
A’
B’
C’
G’
A
B
G
C
q

## Slide 27: A practical problem
A brass sleeve of length L is slipped over a steel bolt and is held in place by a nut that is turned just snug. The nut is tightened by one turn. The pitch of the thread is p. What are the forces developed in the bolt and the sleeve? The area of cross section of the bolt is As , the sleeve is Ab. Modulus of elasticity for steel and brass are Es and Eb respectively.

## Slide 28: A practical problem
FBDs
Nut pushes the sleeve
Sleeve pushes back the nut

## Slide 29: A practical problem
The tightening of the nut means the length of the sleeve should decrease by p. But this will produce a force F in both the bolt and the sleeve which will cause the sleeve to compress and the bolt to expand as see from the FBDs.
The length of the bolt that will affected by this force will be L-p.
Hence new length of sleeve = L-FL/(EbAb)
New length of bolt = (L-p)+F(L-p)/(EsAs)
These must be the same.

## Slide 30: A practical problem
Using the geometrical constraint of equality of length, we can get the force F. Thereafter it will be possible to find out stresses in the bolt and the sleeve and thus we can get an idea about how much can the nut be tightened without causing any damage.