## Slide 1: Thermal Stresses

## Slide 2: Elongation due to heating
We first consider a rod of length L and area of cross section A, made of a material with modulus of elasticity E and thermal conductivity a. The rod is fixed at the end A to a wall
A
B
L

## Slide 3: Elongation due to heating
The rod is heated so that there is a uniform rise in temperature of DT. As a consequence the rod expands by an amount DL. Bear in mind that this is the situation once equilibrium is reached and there is no further change in temperature. We are not dealing with what happens in between, i.e. when the temperature is changing with time.
B’
A
L+ DL
After temperature rise DT

## Slide 4: Strain due to heating
If there is a change in length then there must be strain.
This strain that is due to temperature change is called thermal strain and is given by
B’
A
L+ DL
After temperature rise DT
Thermal strain

## Slide 5: Elongation
The displacement of the free end is the total elongation
B’
A
L+ DL
After temperature rise DT
Elongation

## Slide 6: Stress due to heating
Does it follow that since there is strain there must be stress.
In the current situation, at equilibrium, there is no stress
While elongation was happening there will definitely be dynamic stresses, because molecules/atoms are being moved around. But once the final shape is reached, there is no stress. Since on end is free there is no barrier to the expansion(or contraction). Hence at equilibrium (thermal and mechanical) there is no internal force and hence no stress, despite the strain.

## Slide 7: Statically indeterminate case
This time the rod is fixed at both ends. The rod is heated so that there is a uniform rise in temperature of DT. As a consequence the rod will “want to” expand by an amount DL.
A
B
L

## Slide 8: Statically indeterminate case
The walls will “want to” stay in place.
The walls will push back the rod from both ends.
The rod will push the walls at both ends
A
B
L

## Slide 9: Statically indeterminate case
These statements are captured in the FBD of the rod. The FBD may look odd, because it looks as if the rod is being pulled by the walls.
FRA
FRB
A
B
A
B
Free body diagram
Statics

## Slide 10: Statically indeterminate case
If the rod were cooled then these forces would be opposite. However we can persist with this FBD because in our calculations DT would then be a negative number and the sign of the forces would also change in that case.
FRA
FRB
A
B
A
B
Free body diagram

## Slide 11: Thermal stresses
Since both ends are constrained the thermal strain will now result in a thermal stress
The thermal stress will result in an internal force F trying to cause the rod to expand.
When we cut a section this is the F that we will see
FRA
A
F

## Slide 12: Thermal stresses
For equilibrium F = FRA
You may want to consider what happens if we take a section from the other end. It will tell you why if that end is free there will be no stress (because in case of a free end there will never be a force at end).
FRA
A
F

## Slide 13: Expansion must match contraction
Here we will consider as if there is expansion in case of both the mechanical forces and the thermal forces. It looks odd but once again the signs will come to our rescue.
Thermal expansion
Mechanical expansion

## Slide 14: Expansion must match contraction
Apply the geometrical constraint. As can be seen, one of the DL s must be negative. We can now find the forces.

## Slide 15: Alternative view of the problem
What force F must be applied at the free end of the rod such that a temperature change of DT will not result in any change in length ?
A
B
L
F