## Slide 1: Stress Transformation
Introduction to a tensor approach

## Slide 2: Stress Transformation in 2D
We consider a small surface patch as shown, in an element of volume in a body.
A force DF acts at the center of this surface.
We will be considering only the 2 D version of the problem
So we will look at a section in the X Y plane.
X
Y
Z
DF

## Slide 3: Stress Transformation in 2D
We will now recall some simple ideas about vectors.
Component (scalar) of a vector in direction n is
This component can be represented also as a vector in the direction n as
The remaining (vector) part of the vector is therefore
We will use these ideas both for force and area vectors.

## Slide 4: Stress Transformation in 2D
The 2 D section is now shown along with the coordinate system.
The vector n is the vector normal to the surface.
In 2 D it can be specified in terms of the angle q made by it with the +ve x axis.
The vector s is along the surface and perpendicular to n.
X
Y
DF
DFn
DFs
n
s
q

## Slide 5: Stress Transformation in 2D
We will consider areas as vectors. Thus if the surface patch(shaded) has area DA, then it is designated as
X
Y
Z
q
n
s

## Slide 6: Stress Transformation in 2D
It is easy to see that the components of the area vector are simply the projections on the YZ and ZX planes.
They are also the dot products of the area vector with i and j unit vectors.
X
Y
Z
q
n
s

## Slide 7: Stress Transformation in 2D
In 2 D, the vector n can therefore be specified in terms of the angle q made by it with the +ve x axis.
X
Y
n
s
q

## Slide 8: Stress Transformation in 2D
The force DF can be resolved into two components straight away.
One component DFn is along the unit normal to the surface (n). This direction is unique since a flat surface has a unique normal.
The other component DFs is tangential to the surface.
X
Y
DF
DFn
DFs
n
s

## Slide 9: Stress Transformation in 2D
DFs poses a mild problem in 3 D, since a tangent in 3D is not a line but a surface.
Therefore full information about this component requires that it be split into two orthogonal directions along the surface patch.
For the time being, we leave this problem unresolved and focus on 2D only.
X
Y
DF
DFn
DFs
n
s

## Slide 10: Stress Transformation in 2D
Stress at a point is defined in terms of a vector called the traction vector.
Its magnitude is the ratio of the magnitudes of DF and DA vectors
The direction is that of the DF vector.
X
Y
DF
DFn
DFs
n
s

## Slide 11: Stress Transformation in 2D
We now consider the component of the traction vector along the normal to the area and do some manipulations.
X
Y
DF
DFn
DFs
n
s

## Slide 12: Stress Transformation in 2D
This component of the traction vector is the normal stress.
As we can see, this is simply the ratio of the force component normal to the surface, i.e. the normal force, to the area of the surface.
X
Y
DF
DFn
DFs
n
s

## Slide 13: Stress Transformation in 2D
Next we consider the component of the traction vector along the surface.
Its will simply be the magnitude of the vector difference of the traction vector and its normal component.
X
Y
DF
DFn
DFs
n

## Slide 14: Stress Transformation in 2D
We do some manipulations

## Slide 15: Stress Transformation in 2D
So we now can define this traction vector in terms of stress.
X
Y
DF
DFn
DFs
n
s
q

## Slide 16: Stress Transformation in 2D
So we now can define this traction vector in terms of stress.
X
Y
DF
DFn
DFs
n
s
q

## Slide 17: Stress Transformation in 2D
Let us get back to this figure and investigate the prism
They are also the dot products of the area vector with i and j unit vectors.
X
Y
Z
q
n
s

## Slide 18: Stress Transformation in 2D
Now consider a traction vector T, due to a force DF acting on the inclined shaded area of the prism.
This time we will define it in terms of the x and y components of the forces
X
Y
Z
z
q
n
s
DF
DFy
DFx

## Slide 19: Stress Transformation in 2D
The total force acting on this inclined face is therefore
X
Y
Z
z
q
n
s
DF
DFy
DFx

## Slide 20: Stress Transformation in 2D
Let us consider the traction vector acting on the area DAx . As we have seen it can be expressed in terms of the normal and shear stresses acting on the area on which it acts. Hence
X
Y
Z
z
q
n
s
DF
DFx
DAx
DFy
txy
sx

## Slide 21: Stress Transformation in 2D
Recalling the original definition of a traction vector , we get for traction vector Tx

## Slide 22: Stress Transformation in 2D
Next consider the traction vector acting on the area DAy . Expressing this component as well in terms of the normal and shear stress acting on the area on which it acts, and remembering that txy=tyx, we get
X
Y
Z
z
q
n
s
txy
sy
DAy

## Slide 23: Stress Transformation in 2D
Similarly using the original definition of a traction vector , we get for traction vector Ty

## Slide 24: Stress Transformation in 2D
For equilibrium of the prism sum total of forces acting on the three faces must be zero. Hence

## Slide 25: Stress Transformation in 2D
Separating the components
We can write this in matrix form
This is Cauchy’s stress formula in 2D

## Slide 26: Stress Transformation in 2D
Now consider the individual components
So we can consider an extension of the definition of dot products to matrix multiplication

## Slide 27: Stress Transformation in 2D
A matrix is a column of row vectors and also a row of column vectors
The extended definition means that matrix multiplication is simply taking dot products of the row vectors of the first matric with the column vectors of the second.
Also a column vector is a matrix with a single column and a row vector is a matrix with a single row.
Finally we can now (this is a very loose definition) call our matrix as a tensor.

## Slide 28: Stress Transformation in 2D
So we have a stress tensor
Dot product of this stress tensor with the unit normal vector of an area gives the traction vector.

## Slide 29: Stress Transformation in 2D
The traction vector is also expressed as
We can further use the dot product
In a more compact form

## Slide 30: Stress Transformation in 2D
Thus when we are given the state of stress at a point, then all we need to do to find the normal and shear stress in a particular plane are the following.
Form the stress tensor
Take the dot product of this stress tensor with the unit normal vector of the plane to get the traction vector.
Take the dot product of the traction vector with the unit normal vector of the plane to get the normal stress.
Subtract the square of the normal stress from the square of the magnitude of the traction vector and take square root too get the shear stress.

## Slide 31: Stress Transformation in 2D
Suppose we have a plane with no shear
Let the unit normal vector of the plane be
Using Cauchy’s stress formula in matrix form we have

## Slide 32: Stress Transformation in 2D
However, since there is no shear stress acting on the plane the traction vector is also
We can write this in a matrix form

## Slide 33: Stress Transformation in 2D
We now get a matrix equation in a form we will encounter in a few other subjects known as an eigenvalue equation. The roots of the unknown s are called eigenvalues, while the corresponding direction vectors are called eigenvectors.

## Slide 34: Stress Transformation in 2D
Let us simplify further
We have

## Slide 35: Stress Transformation in 2D
Attempting to solve we get
Thus we can only get a ratio and even that ratio will exist only if

## Slide 36: Stress Transformation in 2D
We thus get a quadratic equation in s, whose solution will give two roots
Once we obtain the roots we can get the ratio n1/n2
We can then use the relation
This will let us find the direction vectors corresponding to the plane of zero shear